## Slide 1
Verification of AXI to AHB Bridge
using UVM
Presented by: Sushant Gautam
Methodology: UVM Based Functional Verification
AMBA Protocol Verification | AXI → AHB

## Slide 2
Project Introduction
AXI Protocol
Advanced eXtensible Interface — high-performance AMBA bus used in complex SoCs for high throughput communication.
AHB Protocol
Advanced High-performance Bus — simpler AMBA protocol ideal for peripheral and memory communication.
AXI to AHB Bridge
Enables seamless communication between AXI masters and AHB slaves with proper protocol translation.
Verification Goal
Verify correct conversion of AXI transactions into AHB transactions and validate protocol behavior across scenarios.

## Slide 3
AXI Protocol Overview
AXI Key Features
Separate Read & Write Channels
Independent Address and Data Phases
Burst Transactions Support
Multiple Outstanding Transactions
High Throughput Architecture
AXI Channels
AW
Write Address Channel
W
Write Data Channel
B
Write Response Channel
AR
Read Address Channel
R
Read Data Channel

## Slide 4
AHB Protocol Overview
AHB Key Features
Single Shared Bus Architecture
Address & Data Phase Pipelining
Burst Transfers Supported
Simpler Protocol vs AXI
Important Signals
HADDR
Address Bus
HTRANS
Transfer Type (IDLE/NONSEQ/SEQ)
HWRITE
Transfer Direction
HWDATA
Write Data Bus
HRDATA
Read Data Bus
HREADY
Transfer Complete Indicator
HRESP
Transfer Response (OKAY/ERROR)
AXI vs AHB
AXI is feature-rich with separate channels for high performance. AHB offers simplicity with a shared bus suitable for peripherals.

## Slide 5
AXI to AHB Bridge Architecture
AXI Master
AXI2AHB Bridge (DUT)
AHB Slave
▼
▼
Bridge Functions
→
Address Translation
Maps AXI addresses to AHB address space
⇄
Data Transfer Conversion
Converts data widths and formats between protocols
↩
Response Conversion
Translates AHB HRESP to AXI BRESP/RRESP
▸▸
Burst Handling
Breaks AXI bursts into sequential AHB transfers
⚡
Error Propagation
Forwards error conditions across protocol boundary

## Slide 6
Verification Objectives
Verify AXI Write Transactions
Verify AXI Read Transactions
Verify Address Translation
Verify Data Translation
Verify AHB Response Handling
Verify Reset Functionality
Verify Error Conditions
✓ Success Criteria: Expected AXI transactions must match actual AHB transactions observed at the output

## Slide 7
UVM Testbench Architecture

## Slide 8
Agent Architectures
AXI Agent
AXI Driver
Receives sequence items and drives AXI signals on the interface.
AXI Monitor
Captures AXI transactions and forwards them to the scoreboard.
AXI Sequencer
Controls transaction flow from sequences to the driver.
AHB Agent
AHB Driver
Generates AHB responses: OKAY, WAIT states, and ERROR responses.
AHB Monitor
Observes actual AHB transactions on the bus interface.
AHB Sequencer
Orchestrates response sequences to simulate various slave behaviors.

## Slide 9
Sequences & Scoreboard
Virtual Sequencer
Coordinates multiple agents and provides centralized control for complex test scenarios.
1. Reset Sequence
2. AXI Write Sequence
3. AXI Read Sequence
4. Error Response Sequence
5. Wait State Sequence
Scoreboard
AXI Monitor → Expected Tx
▼
AHB Monitor → Actual Tx
▼
COMPARE
✓ Address Integrity
✓ Data Integrity
✓ Response Integrity

## Slide 10
Waveform Results – Write Flow
AXI Write → AHB Transaction Flow
1
AWVALID + AWREADY (both 1)
AXI Write Address Handshake –address accepted by the bridge
2
WVALID + WREADY (both 1 )
AXI Write Data Handshake – data accepted by the bridge
3
HTRANS =2 , HADDR = AWADDR
Bridge initiates AHB transfer – HTRANS =2 means NONSEQ, start of valid AHB transfer
4
WDATA = HWDATA
Data translations is successful
5
BRESP Returned & HRESP Generated
AXI Write Response to master & AHB Slave provides response
Observations
✅ Write Conversion
Successful conversion of AXI Write into AHB NONSEQ transfer verified.
📊 Protocol Timing
Address and data handshakes occur per protocol spec with proper phase sequencing.
🔄 Response Path
BRESP correctly returned to AXI master after AHB HRESP observed.

## Slide 11
Waveform Results

## Slide 12
Challenges & Learnings
⚠ Challenges Faced
UVM Configuration Database Issues
Virtual Sequencer Connections
Reset Agents Configuration
Agent Configuration Propagation
Scoreboard Synchronization
Debugging Protocol Timing
✓ Key Learnings
AXI Protocol Internals
AHB Protocol Internals
UVM Architecture & Flow
Functional Verification Flow

## Slide 13
Conclusion
Successfully developed UVM Verification Environment
Verified AXI to AHB transaction conversion
Verified reset, write, read, wait-state & error scenarios
Implemented monitors, drivers, sequencers & scoreboard
Captured protocol-level waveforms validating bridge functionality
Future: Regress Functional Coverage • All possible SVA Assertions • Corner Case Testing
Thank You